## Slide 1
Numerical Modelling in coastal areas:
Case studies from the Italian Institute for Environmental Protection and Research
Antonello Bruschi, Luca Liberti & Francesco Lalli
Italian Institute for Environmental Protection and Research (ISPRA)
MedGOOS Half-Day Seminar
“Exchanging Numerical Coastal Modelling Experiences for Applications in the Mediterranean Region”
5th March 2010 - Istanbul

## Slide 2
Coastal areas
Hydrodynamic
Sediment transport
Water quality
Biogeochemical & ecological modelling
Navigation
Erosion
Bathers health
Hazard issues
Marinas & Harbours
…
Energy production
Numerical models in coastal areas: Applications

## Slide 3
Case study 1: Erosion at San Benedetto del Tronto: Adriatic sea

## Slide 4
Breakwater
Northern limit
Selected Area
Tronto River
Southern limit
Shoreline 2008
Shoreline 2000
Notes: Utilizzo del modello Delft per lo studio degli effetti di mareggiate significative per differenti intensità e direzioni di provenienza.

## Slide 5
In the last 50 years the beach moved back of about 100 m due to erosion.
Both North and South of the selected area the coastline is protected by breakwaters.
Tasks:
Off-shore waves data (measured by a buoy);
Wave propagation from off-shore to near-shore;
Study of the shoreline evolution through aerial photo (from 1894 to 2008);
Sediment analysis;
Bathymetric survey;
Solutions planning;
Numerical modelling with GENESIS for evaluating the effects of each proposed solution;
Numerical modelling with Delft3D for evaluating the effects of sea storms;
Conclusions, design of the selected structures and budget estimation.
OBJECTIVE: Prevent further erosion
Notes: Utilizzo del modello Delft per lo studio degli effetti di mareggiate significative per differenti intensità e direzioni di provenienza.

## Slide 6
Breakwaters (n.6):
  Parallel to the shoreline
  Depth -3.2 m m.s.l.;
  Length 260 m;
  Gap length 30 m;
  Submergence -0.5 m m.s.l.;
  Breakwaters slope 2:1
Nourishment protected by breakwaters
Shoreline 2008
Nourishment:
30 m added to the shoreline
position (shoreline 2000)

## Slide 7
The long term effect of the proposed solutions has been simulated with several scenarios using GENESIS (a one line model).
One line models use a simplified formulation in order to simulate the shoreline evolution for many decades.
Many physical processes are not taken into account by the one line model: - there is no cross-shore sediment transport; - the bottom profile is assumed to follow the Dean’s law.
Only short term simulations are possible with more complete models.
The effect of a few sea storms have been simulated using the Delft3D suite of models, in order to check the response of the structures to extreme events.
Numerical models application

## Slide 8
Delft 3D
Three modules of the Delft3D have been used:
  Wave model (SWAN): Wave propagation model;
  Hydrodinamic model: 2D/3D current field;
  Sediment transport model: sediment suspension, deposition

## Slide 9
Selected
storms
Boundary
conditions
Scenarios
description
Scenario | Rt (years) | Dir (°N) | Hs Max (m) | Date
1 | 5 | 35 – 65 (NE) | 3.4 | 1-5 Jan 1993
2 | 50 | 35 – 65 (NE) | 4.3 | 25-28 Dec 1996
3 | 5 | 65 – 95 (E) | 3.0 | 8-12 Dec 1990
4 | 15 | 65 – 95 (E) | 3.5 | 6-9 Nov 1999
Delft 3D
Through the extreme event analysis (POT) 4 storm events have been selected. Two events for each of the two more frequent incoming wave directions. All the events come from the data set. One event for each direction corresponds to the 5 years return value, while the other one is the stronger storm in the data set form that direction.
Only wave action and river discharge have been considered. Wind action, large scale currents and tides were not taken into account.

## Slide 10
Delft 3D
Computational grid: 108 by 270 cells with a resolution up to 10 m

## Slide 11
Dean equilibrium profile
Natural bathymetry
Breakwater
Delft 3D
Breakwaters and bathymetry
Section view

## Slide 12
Delft 3D
Boundary conditions
Off-shore waves
Tronto River outflow
Sediment features
Sediment class: sand, D50= 0.2 mm
There is no sediment input from the river
Significant wave height, period and direction
Currents
Bathymetry
  Wave model
  (SWAN)
  Hydrodynamic model
  Morphodynamic
  model
Bathymetry

## Slide 13
Sediment transport during the sea storm
Simulation
Delft 3D
Sea Storm n.1
Rt 5 years - Direction NE

## Slide 14
Sediment transport during the sea storm
Simulation
Delft 3D
Sea Storm n.2
Rt 50 years - Direction NE

## Slide 15
Sediment transport during the sea storm
Simulation
Delft 3D
Sea Storm n.3
Rt 5 years - Direction E

## Slide 16
Sediment transport during the sea storm
Simulation
Delft 3D
Sea Storm n.4
Rt 15 years - Direction E

## Slide 17
Case study 2 – Evaluating the wave climate in front of the Bojana River and its effect on the river outflow.

## Slide 18
Large scale model
Adriatic Sea
Wave generation due to wind action
Small scale model
Hi-resolution near Bojana river mouth
Nesting
Wave propagation from off-shore to near-shore

## Slide 19
ECMWF wind data: 2004 - 2008
Nested grid (one-way):
Longitude: 19.25oE – 19.5oE
Latitude: 41.75oN – 41.90oN
Resolution (regular grid):
Longitude 401 grid points – about 50 m
Latitude 241 grid points – about 70 m

## Slide 21
Bojana river mouth area – Bathymetry

## Slide 22
Map of measurement instruments

## Slide 23
Scatter-plot with linear regression - Monopoli
Numerical model – Hm0 (m)
Measured data – Hm0 (m)

## Slide 24
Interval | Coefficient
0.5 m <= Hm0 < 1.0 m | 0.6247
1.0 m <= Hm0 < 2.0 m | 0.6174
2.0 m <= Hm0 | 0.5486
Calibration by significant wave height intervals
It was used only one coefficient: 1.67 =1/0.6 for waves higher equal than 0.5 m.

## Slide 25
Calibrated Wave Climate: 2004 – 2008. Depth 10 m
Lower than 0.25m = 66%
0.25 – 1.0 m
1.0 – 2.0 m
2.0 – 3.0 m
3.0 – 4.0 m
> 4.0 m
2%
4%
6%
8%

## Slide 26
LONG WAVE CASE:
Shallow Water approximation
Eddy viscosity:  = 0 + t
t = C H u Fischer (1973), Nezu (1996)
Notes: 26

## Slide 27
River flow (waveless condition)
Notes: 27

## Slide 28
River flow (wave length = 62m, T = 5.6”, H = 1m)
Notes: 28

## Slide 29
Conclusions
There are many issues in coastal areas to which numerical models could be applied. Each issue could require a specific schematization of the physics involved, and even the same issue could be approached in different ways, according to the aim of the study.
In this presentation three different ways of approaching waves simulation in coastal areas are shown. Two of them use the same numerical model but in a different way. The last one is based on a completely different approach.
The same happens for circulation models.
Generally, in order to be able to carry out a case study in coastal areas more than one numerical model is required. This is due to the variety of spatial and temporal scales that characterise the coastal phenomena.